## Slide 1
28-BIT FUNCTIONING
COMPUTER SYSTEM
CPU + MEMORY
CACHE
BOOTH MUL
DMA
DESIGNING A
LOGISIM
Page 01

## Slide 2
Introducing our Undergrad Engineers
01
DATAPATH & ALU
Shemonty 2407107
02
CONTROL UNIT
Ratul 2407108
03
ARITHMETIC
Mahima 2407106
05
CACHE & DMA
Thowai 2407109
04
MEMORY SYSTEM
Rup 2407109
28-bit Computer Designing
Computer Architecture Laboratory
LOGISIM
Page 02

## Slide 3
CONTROL UNIT
ROM + FSM
DATAPATH
REGISTERS + ALU
ARITHMETIC
BOOTH MUL
DMA BLOCK COPY → CACHE STAYS COHERENT
What Are We Building?
Page 03

## Slide 4
PC
IR
REGISTER FILE
R0–R15
28-bit
ALU
28-bit
CACHE
16 lines
MAIN MEMORY
4K × 28
CONTROL UNIT • Opcode Decoder • FSM
BOOTH MUL • DMA
System Architecture
Page 04

## Slide 5
The Finished Circuit
Computer_28bit.circ • main circuit, screenshot from Logisim 2.7.1

## Slide 6
REGISTER FILE
R0 R1 R2 R3
R4 … R15
28-bit each
MUX A
MUX B
28-BIT ALU
ADD / SUB
AND / OR / XOR
SHIFT
EQ / LT
RESULT
ADDR • PC / EA
CACHE • Data
IR • Instruction
PC • Next
01
DATAPATH & ALU
Shemonty 2407107
Datapath & ALU
Core idea: registers hold state → ALU transforms it
→ result is written back.
Designing Architect: Shemonty
Page 05

## Slide 7
Datapath
PC, IR, 16-register file, ALU, Booth unit, write-back mux

## Slide 8
FETCH
PC → address
Cache read
DECODE
IR → opcode
Select registers
EXECUTE
ALU / MUL
MEMORY
Cache / RAM
for LOAD/STORE
WRITEBACK
Result → Rd
OPCODE → CONTROL SIGNALS
02
CONTROL UNIT
Ratul 2407108
Control Unit
Designing Architect: Ratul
A multi-cycle FSM turns an instruction into an ordered sequence of control signals.
Page 06

## Slide 9
Control Unit: ROM + State Register
1024 × 28 control ROM, addressed by {state, opcode}

## Slide 10
03
ARITHMETIC
Mahima 2407106
MUL IN: 28-bit × 28-bit
A
Q
Q−1
BOOTH FSM
Shift • Add/Sub • Repeat
28 STEPS: one per clock
Q
M
29-BIT ADDER
+M • −M • 0
MUL
LOW 28
MULH
HIGH 28
DONE
FLAG
Arithmetic Accelerator
Designing Architect: Mahima
The 56-bit product is built over 28 clocks with one adder, so the main ALU stays small.
Page 07

## Slide 11
Booth Multiplier
M, A, Q, Q−1 and a counter around one 29-bit adder

## Slide 12
04
MEMORY SYSTEM
Rup 2407109
Memory System
Designing Architect: Rup
A 16-line direct-mapped cache sits between the CPU and 4K × 28-bit main memory.
TAG
INDEX
WORD
00
0
TAG
28-bit DATA
01
1
TAG
24-bit DATA
02
0
TAG
24-bit DATA
03
0
TAG
24-bit DATA
TAG MATCH?
VALID = 1
HIT
MISS
MAIN MEMORY • 4K × 28-bit
Page 08

## Slide 13
05
CACHE & DMA
Thowai 2407109
CPU
DMA rd,ra,len
DMA
takes the bus
RAM
read source
RAM
write dest.
CACHE
invalidate line
CPU
resumes
!
Page 09
DMA CONTROLLER
Designing Architect: Thowai
DMA BUSY
!

## Slide 14
DMA Controller
Two cycles per word; every write clears the matching cache line

## Slide 15
Instruction Set (32 opcodes, 9 shown)
Opcode
Instruction
Operation
Type
000010
ADD Rd,Ra,Rb
Rd ← Ra + Rb
R
000011
SUB Rd,Ra,Rb
Rd ← Ra − Rb
R
011011
SHLI Rd,Ra,n
Rd ← Ra << n
I
001101
LDI Rd,imm
Rd ← imm
I
010000
LD Rd,[Ra+imm]
Rd ← MEM[Ra+imm]
M
010001
ST Rd,[Ra+imm]
MEM[Ra+imm] ← Rd
M
010100
BNE Rd,Ra,addr
if Rd ≠ Ra: PC ← addr
B
001010
MUL Rd,Ra,Rb
Rd ← low28(Ra × Rb)
A
011010
DMA Rd,Ra,len
copy len words Ra → Rd
D
Page 10

## Slide 16
How an Instruction Executes?
Let us see an Example
ADD R1,R2,R3
F
Fetch
D
Decode
E
ALU ADD
W
Write R1
MUL R1,R2,R3
F
Fetch
D
Decode
S
Start MUL
I
Iterate
I
Iterate
W
Write
Page 11

## Slide 17
Integration & Verification
We integrate bottom-up so every module is testable before the final CPU run.
1
UNIT TEST
ALU + registers
Known operands → expected result
2
CONNECT
Datapath + FSM
Single-cycle ADD/SUB first
3
EXPAND
Cache + RAM
LOAD/STORE + HIT/MISS
4
ACCELERATE
Booth multiplier
Edge cases: −2^27
5
HARDEN
DMA + demo
Copy a block, cache stays right
6
FINAL
Program execution
Fetch → decode → execute → repeat
SUCCESS = matches the golden model + visible HIT/MISS + verified DMA copy
Page 13

## Slide 18
Results: checked in real Logisim 2.7.1
How we tested
• A Python instruction-set simulator, written separately from the circuit, runs every program too
• The circuit runs headless in Logisim 2.7.1; we compare every value written to Out
• 4 hand-written programs + 37 random programs
• All match, including Booth edge cases like (−2^27) × (−2^27)
Demo program
• 818 instructions executed, 17 output values, all correct
• 10! = 3628800; 123456789 × 98765432 = 45423444 × 2^28 + 195687384
• Cache: 914 look-ups, 208 misses, 706 hits (about 77% hit rate)
• DMA copy of 32 words verified by a checksum
• Not built: divider and parity (future work)

## Slide 19
FROM LOGIC GATES
TO A WORKING COMPUTER.
ALU
FSM
BOOTH
CACHE
DMA
The final system demonstrates how computation, memory, control and reliability cooperate inside a CPU.
Page 14

## Slide 20
01
Shemonty
Shemonty 2407107
02
Ratul
Ratul 2407108
03
Mahima
Mahima 2407106
05
Thowai
Thowai 2407109
04
Rup
Rup 2407109
28-bit Computer Designing
Page 15
THANK YOU
Computer Architecture Project
LOGISIM